## Slide 1
IEEE-IAS Annual Meeting & World Conference on
Industrial Application of Electrical Energy, Rome, Oct. 8-12. 2000
Presentation of the paper: “The Influence of Control Strategies on the Energy Capture of Wind Turbines”
(Conf. Rec. Vol. 2, page 886-893)
First, I’d like to introduce Mr. Hoffmann, who is doing research work in this area during his Ph.D. studies at Darmstadt University of Technology, Department of Power Electronics & Control of Drives.
After a short introduction we will consider the basic characteristics of 8 diffe-rent concepts of horizontal axes wind turbines. The analysed concepts cover practically all types of wind turbines which are on the market today. All the different concepts are compared regarding their energy production using simulation models. Finally, we will discuss the simulation results.

## Slide 2
As we will see, many different concepts of wind turbines compete at the market.
One of the most interesting features of a wind turbine is its energy production.
Other features like Power Quality may also be of great concern, but in this work we concentrate on energy production.
In the literature, there exist some comparisons between variable and constant speed wind turbines.
But the authors disagree widely in the figures of merit. The range is from 2% to 38%..
From our paper, we will see, how energy production depends on various parameters
To analyse the system, first let’s have a look to the way, how the torque of a wind turbine is produced.

## Slide 3
In the lower part, we see the rotor of a wind turbine, the wind is coming from the front.
If we take a look from the top to a cross section of the vertical blade, we see the profile.
The wind is coming from the front and is represented by this blue vector
As the blade is rotating, the blade sees the additional wind speed component VB.(green vector)
These two vectors give the resulting wind from the blade’s point of view.
Perpendicular to the resulting wind, the profile produces a lifting force and aligned to the wind a small dragging force
This two form the resulting aerodynamic force, which is decomposed into a thrust force, which the tower has to withstand, and the torque producing force, that is the only one we are interested in

## Slide 4
Each turbine is designed to produce its rated power at a certain wind peed, which we call rated wind speed.
The power inherent in the wind shows a cubic increase with wind speed.
For wind speeds above the rated one, it is necessary to limit the mechanical power generated by the rotor to the rated value of the plant.
The mechanical power can be limited either by stall or by pitch methods.

## Slide 5
The simplest design uses the passive stall method.
In this design,the angle  is always constant,no mechanism to turn the blades around their axes is necessary.
When the wind speed increases, the angle , which is the angle of attack, increases.
Above a certain angle  the stall effect occursand the torque producing force can be limited approximately to its rated value.

## Slide 6
If there is a mechanism to turn the blades around their axes, at low winds a control loop will use this feature to maximise the energy capture.
With higher wind speeds, stall can be enforced in order to limit the torque to its rated value.
In this case, angle  is decreased, the blade acts like a wall in the wind

## Slide 7
When limiting the power by the pitch method, the blades are turned towards the direction of a flag in the wind by increasing the angle .
In this case all aerodynamic forces are reduced.

## Slide 9
As we have just seen, there are three methods to limit the power during strong winds.
When the wind is low, an adaptation of the turbine’s speed to the wind- speed has to be considered.
In the simplest case, no speed adaptation is implemented. In this classical single speed concept a gear and an asynchronous generator is used.
When a pole changing asynchronous generator is used, a limited speed adaptation is realized. Typically, two speeds are used in this case
Full speed adaptation calls for a variable speed concept. Here a power electronic converter is always necessary. In our paper, we only took the gearless, direct driven synchronous generator into consideration for a variable speed wind turbine
To our knowledge, there is no active stall, variable speed turbine on the market.
This matrix containing 8 different concepts covers the vast majority of wind turbines on the market.
To compare 8 different wind turbines, all must be exposed to identical conditions.
With real wind turbines, this would be an extremely expensive approach.
Therefore, we use a simulation of the different wind turbines in this paper.

## Slide 10
The simulation of the wind must contain all average wind speeds and all levels of turbulence which may appear in reality.
Here is an example of a wind simulation with an average speed of 9m/s and a turbulence level of 20%.
The turbulence is generated by random numbers and is fitted by practical values of the acceleration of the air.
Here, the output power of a constant speed,pitch controlled 600kW turbine is shown .
For the above depicted wind, the average power is 400kW, but the actual power fluctuates between 700kW and Zero. Instead of feeding a nearly constant power to the grid, the constant speed turbine creates a rather poor power quality.
The overshoot in power during a wind gust is due to the limited velocity of the pitch drives. It takes some time, till the angle  is increased to the power limiting value

## Slide 11
The turbine’s power is proportional to the 3. power of the wind speed and the turbine’s characteristic, which is a function of the tip speed ratio 
The losses of the gear and the generator are subtracted to give the output power. The losses are a function of the turbine’s power.
Next, we discuss some simulation models for the plant.
The most simple concept is the constant speed, passive stall concept. Here, the speed and the angle are constant. The wind speed from the previous figure enters at the right side

## Slide 12
When we consider a constant speed, pitch controlled concept, we have to add the pitch control part.
There are three operating areas.
If the turbine produces more than rated power, the switch is in the upper position and the angle  is constantly increased with its maximum speed of 6°/s.
If the power is near the rated power, the pitch drive is stopped and  remains constant.
If the power is below rated power, the switch is at the bottom position and a closed control loop with a proportional controller (Kp) is formed. This controller gets its reference from a characteristic, which gives the optimum angle  as a function of the power.
With this optimum angle  the maximum power is produced, when the wind is below its rated value

## Slide 13
Next we consider a variable speed concept where power is limited by stall.
In the upper part, the rotating masses are represented which are accelerated by the
difference of the generator’s and the turbine’s torque.
When the wind is below its rated value, the maximum power is produced if the torque of the generator is proportional to the square of the speed. The converter and the generator are very fast acting devices. So their time delay in the upper loop can be neglected.
But of course the losses of the converter and the generator have to be considered to find the power which is fed into the grid.

## Slide 14
A combination of average wind speed and turbulence is applied for 5 min. of real time to the simulation model.
The result is the average power which is fed into the grid within these 5 minutes. This power is represented by one of these squares of this surface.
We have to repeat this simulation for each combination from 23 discrete average wind speeds and 6 turbulences which gives 138 simulations.
As we compare 8 different concepts, we have to repeat this procedure for each concept. (-> 1000 simulations)
Additionally we want to investigate the influence of some design parameters.
We compare 3 different design tip speed ratios and 2 different profiles which gives a total of 6000 simulations.
For a given turbulence, we can cut one slice out of this figure.

## Slide 15
Then we see the output power as a function of the wind speed for a specific turbulence.
For the energy production at a given site, the wind speed is decisive . A wind map gives the average annual wind speed for each location.
In this example, we have an average annual wind speed of 7m/s. The actual wind of course may be quite different.
In this paper we use a Rayleigh distribution, which gives the time duration for each discrete wind speed within one year. The sum of all these time-bars is 8700h.
The energy produced under these conditions is found by multiplying power and time. The sum of all these energy-bars gives the total energy produced within one year.
This is the only number we are interested in.

## Slide 16
Now we come to discuss the results. Here, we see the performance of the 8 different concepts when different average annual wind speeds are applied. The turbulence level is 10%. First of all we have to note, that the most simple concept, which is the single speed, passive stall concept, is used as baseline. We see the gain in energy production of the more sophisticated concepts over the most simple one. The different concepts are identified by their speed (single, two or variable speed) and the method power is limited (stall or pitch).
The message is, that for a low average annual wind speed, speed adaption of the rotor is interesting.
For the two-speed machines, the gain in energy production is 9-11%. The gain of the variable speed machines is 17-18%. For sites with a high average wind, all turbines are operated at their power limit for a considerably long time in the year. At the limit of power, all produce a rather similar energy.
Therefore, the differences are smaller for high average annual wind speeds.

## Slide 17
Next result: Here the average wind speed is constant 7m/s, but different levels of turbulence are applied. The gain of the speed adapting, stall controlled machines decreases for high turbulence levels. The reason is, that speed adaptation cannot be carried out in the short time of a wind gust. Instead, the wind gust stalls the rotor and energy is lost.
In contrast to this, the gain of the constant speed, pitch controlled machines increases for high levels of turbulence. The reason is, that the pitch angle to limit the power during a wind gust is rather large and the pitch drives are not fast enough to limit the power. Therefore, in this two cases, an overshoot in power above the rated value occurs, which increases the energy.

## Slide 18
Next we change design parameters. Here, the design tip speed ratio
is varied. First, it is important to note, that the absolute energy capture of the refe-rence concept decre-ases with increasing tip speed ratio. But the benefit of a higher tip speed ratio is a reduced mechanical stress on all components, as with a higher speed the same power is produced with
a lower torque. With a lower torque, all aero-dynamic forces will be lower.
We can easily see, that for all concepts, a higher tip speed ratio increases the gain in energy. The variable speed concepts take the greatest benefit from a high tip speed ratio. This means, that a variable speed machine will pay off better, if a high tip speed ratio is selected. But the drawback of a high tip speed ratio is the high acoustic noise.

## Slide 19
In this figure, the annual average wind speed is constantly 7m/s and different levels of turbulence are applied.
In contrast to the last but one figure, here we use a different profile, which also calls for a different design tip speed ratio, as the power characteristic of profile 2 (Goe 535) is flat compared to the first one (Goe 785).
With profile 2, the gain in energy is higher for all concepts except for the passive stall controlled concept. Additionally, here the gain is rather constant for all levels of turbulence. Especially, there is a benefit for the pitch controlled, variable speed concept at high levels of turbulence with this profile.

## Slide 20
Finally, for a high design tip speed ratio different average annual wind speeds are applied . As can be seen easily, in all cases the gain in energy increases with a high design tip speed ratio, especially at low winds. The gain of the variable speed concepts nearly reaches 30%. But unfortunately, the combination of low average annual wind
speed and high design tip speed ratio is probably unrealistic. The low wind speed is characteristic for an interior site. But there, the higher acoustic noise due to the high design tip speed ratio may not be tolerated. For an offshore site, where the acoustic noise would be no severe problem, typically the wind is strong. But for strong winds, the gain in energy for all the sophisticated concepts is not so impressive.

## Slide 21
Conclusion:
First result:
Most differences in literature can be explained by different conditions.
But much more important is the second result:
For a given site, a wind atlas shows the average annual wind speed and the turbulence.
These data are inputs to the simulation. From the simulation, we get the energy capture of 8 different concepts.
The price for the real wind turbines has to be asked from the manufacturers.
Then the price to energy ratio is known, which is a rather important criterion for a final decision.
An additional aspect for a final decision is “Power Quality”. Variable speed turbines typically provide better power quality, as energy from wind gusts can partially be stored in the rotating mass.